Neural Network Procedure - Setup
1) Represent your input data as an N-dimensional array, I, e.g.
- handwriting recognition – 784 pixel values (28x28)
- PID – p, theta, phi, nphe, beta, Edep, …
   the values should be normalized so the range is 0.01 – 1.00 (avoid exactly zero)
2) Represent the possible outputs as an M-dimensional array, e.g.
- handwriting recognition – (0, 1, …, 9) and/or (a, b, …, z) and/or (A, B, …, Z)
  and represent a specific output, T (for target), as (0.01, 0.01, …, 0.99, …, 0.01, 0.01) (e.g.)
3) Select a value for H – the number of hidden nodes (100 is reasonable), and L – the learning rate (0.3 is reasonable). These can be tuned later.
4) Construct the weight matrices Winput, hidden and Whidden, output . The dimensions of Wih and Who will be H x N and M x H, respectively. Their elements should be distributed randomly based on a gaussian distribution with a mean of zero and standard deviations of 1/sqrt(H) and 1/sqrt(M), respectively.
5) Define an activation function A(x), e.g.
A( x ) = { 1 } over { 1 + e^{-x} }

---
Neural Network Procedure - Training
1) Calculate the following quantities: hidden inputs (HI), hidden outputs (HO), final inputs (FI), final outputs (FO), output errors (OE), hidden errors (HE), where,
HI = Wih * I
HO = A(HI)
FI = Who * HO
FO = A(FI)
OE = T – FO
HE = WhoT * OE
  where A(matrix) simply acts on each element in the matrix.
2) Update the weight matrices:
Who → Who + L * (OE * FO * (1.0 – FO)) * HOT)
Wih → Wih + L * (HE * HO * (1.0 – HO)) * IT)
3) Iterate over the whole training sample

---
Neural Network Procedure – Querying
1) Represent your input data as a normalized N-dimensional array, I, as previously described
2) Calculate HI, HO, FI, FO as previously described
3) FO will be an M-dimensional array. The output corresponding to the largest value in FO will be the networks best guess at an answer.